## Slide 1
Guru Nanak Dev University
PS-21
Low power slam for planetary Exploration
Team Name
GURKIART SINGH (Team Lead) ▪ BHAWARDEEP SINGH ▪ DEV GROVER
BuildFest 2.0
Department of mechanical engineering

## Slide 2
PROJECT BRIEF · 2026
PS-21
Low-Cost Autonomous Rover
Proof-of-Concept for Visual-Inertial SLAM and 2D Hazard Mapping under Space-Grade Compute Constraints.
VIO SLAM
≤150 MB RAM
ROS 2
Planetary Robotics Working Group · Internal Review
Team name: Ternary Tensors
Notes: Open the deck and introduce PS-21 as a low-cost autonomous rover proof-of-concept. Name the dual mission: monocular VIO SLAM plus a continuously updated 2D hazard grid. Call out the organizing constraint — everything runs inside ≤150 MB of RAM on Pi 4-class hardware. Frame the talk as a hardware + algorithmic pipeline review: chassis → compute → front-end → back-end → terrain. Set the tone: cheap parts, space-grade discipline, real autonomy.

## Slide 3
PS-21 · LOW-COST AUTONOMOUS ROVER
02 / 12
MISSION PROFILE
An untethered rover that maps terrain it cannot afford to forget.
PS-21 is a budget-friendly, untethered mobile rover built to validate autonomous planetary exploration on commodity hardware. It carries its own power, compute, and sensing — no tether, no offboard processing — and is designed to demonstrate that real Visual-Inertial Odometry and hazard mapping can run inside the kind of computational envelope a real mission would impose.
The proof-of-concept targets two simultaneous deliverables: a real-time monocular VIO estimate that resolves scale ambiguity using inertial cues, and a continuously updated top-down 2D hazard grid that flags terrain too rough or steep to traverse. Together they form the minimum viable autonomy stack for a low-cost planetary scout.
≤150 MB
RAM BUDGET
Pi 4
COMPUTE TARGET
VIO + 2D
CORE OUTPUTS
4WD
MOBILITY
PS-21 · MISSION PROFILE
02
Notes: Open with why untethered matters — onboard power, compute, and sensing make this a real mission proxy. Explain the dual-output philosophy: VIO pose estimate plus a live 2D hazard grid are inseparable deliverables. Frame the 150 MB RAM ceiling as the organizing constraint — every design choice answers to it. Walk the four right-side stats as the proof-of-concept's operating envelope. Tee up the rest of the deck: hardware first, then algorithm, then output.

## Slide 4
PS-21 · LOW-COST AUTONOMOUS ROVER
03 / 12
THE CHALLENGE
Real autonomy, simulated space-grade limits.
▦
Memory Ceiling
A hard ≤150 MB RAM cap on the host. Sliding-window optimization, keyframe marginalization, and Chow-Liu sparsification all exist to keep the factor graph inside this envelope — not as an optimization luxury.
✦
Compute Footprint
Raspberry Pi 4-class CPU is the reference target. Front-end feature extraction and optical flow must run cheaply enough to leave headroom for back-end optimization and the hazard pipeline.
◉
Monocular Scale Ambiguity
A single camera cannot recover metric scale. The 200 Hz IMU is not optional — it is the only way to resolve scale and keep VIO trajectories physically meaningful on rough terrain.
Every algorithmic choice is downstream of one number.
150 MB of RAM is not a target — it is the constraint that shapes the front-end, the back-end, and the terrain pipeline alike.
PS-21 · CONSTRAINTS
03
Notes: Open with the constraint-first mindset — every design decision answers to a number, not a preference. Walk the three pressure points in order: memory ceiling (RAM), compute footprint (CPU), and monocular scale ambiguity (sensor). Stress that the 200 Hz IMU is mandatory, not optional — without it, monocular VIO has no metric scale. Use the navy band as the takeaway: 150 MB is the constraint, not a target. Bridge to the rest of the deck: each pipeline stage is shaped by these three limits.

## Slide 5
01 / 02
Hardware Architecture
Chassis, actuation, and the onboard compute + sensing stack that PS-21 carries into the field.
Notes: Transition into the hardware walk-through — chassis first, then the compute and sensing stack.

## Slide 6
PS-21 · HARDWARE ARCHITECTURE
05 / 12
CHASSIS & ACTUATION
A rugged 4WD platform built around commodity drive components.
◔
4-Wheel Drive Chassis
Rugged skid-steer platform with four driven wheels, sized for indoor and outdoor prototype terrain. Geometry tuned for stable monocular capture while crossing small obstacles.
⚙
100 RPM Johnson Motors
Geared Johnson DC motors at each wheel. Torque and speed balanced for slow, controlled traversal — the regime where VIO feature tracks stay stable across frames.
✦
Dual-Channel Motor Driver (L293D)
L293D-class driver routes PWM from the Arduino Nano to the motor pairs. Direction and enable lines give skid-steer differential control with minimal wiring overhead.
⚡
Untethered Power
Onboard battery supply — no tether, no external rail. Power budget sized to keep compute, vision, and drive all running for a full mission-length traversal.
Reference: 4WD robotic chassis with knobby tires and perforated deck — PS-21 uses an analogous prototype platform.
PS-21 · HARDWARE
05
Notes: - Skid-steer geometry keeps the build mechanically simple and lets the rover turn on the spot. - Slow 100 RPM Johnson motors keep inter-frame displacement small so VIO feature tracks stay stable. - L293D dual-channel driver trades efficiency for wiring simplicity — direction + enable lines cover skid-steer. - Untethered power is non-negotiable: compute, vision, and drive all share one onboard battery budget.

## Slide 7
PS-21 · HARDWARE ARCHITECTURE
06 / 12
COMPUTE & VISION STACK
Three devices, one onboard pipeline.
PS-21 splits perception, low-level control, and wireless bridging across three cheap, swappable modules — each chosen so the failure of one does not collapse the rest.
VISION + WIRELESS
◉
ESP32-CAM
OV2640 monocular sensor · Wi-Fi bridge
Dual-purpose module. The OV2640 sensor captures monocular frames for the VIO front-end, while the ESP32's Wi-Fi radio streams the video feed to the host laptop and receives movement commands — eliminating a separate wireless link.
2 ROLES · 1 BOARD
LOW-LEVEL CONTROL
▦
Arduino Nano
Hardware slave · IMU reader · PWM driver
Reads high-frequency IMU samples over I2C and drives motor PWM outputs. Programmed via the ESP32-CAM serial bridge as a workaround for the missing Mini-USB cable — a deliberate bootstrapping hack to keep the build moving.
200 HZ IMU READ
INERTIAL SENSING
✦
MPU-6050
6-axis IMU · I2C · chassis-center mount
A 6-axis MEMS IMU mounted flat at the exact geometric center of the chassis deck. Samples motion at 200 Hz, feeding the back-end with the inertial cues needed to resolve monocular scale ambiguity on rough terrain.
6-AXIS · 200 HZ
PS-21 · COMPUTE STACK
06
Notes: - Three cheap, swappable boards: a single-board failure doesn't collapse the autonomy stack. - ESP32-CAM pulls double duty — monocular vision for VIO plus the Wi-Fi command/video link, no extra radio. - Nano is flashed over the ESP32-CAM serial bridge as a deliberate workaround for the missing Mini-USB cable. - MPU-6050 is mounted flat at the chassis geometric center so inertial readings reflect true body motion. - Role split: ESP32-CAM = vision + comms, Nano = low-level control + IMU read, MPU-6050 = inertial cues.

## Slide 8
PS-21 · HARDWARE ARCHITECTURE
07 / 12
ODOMETRY & INERTIAL SENSING
Wheel encoders and a 200 Hz IMU back the visual estimate.
WHEEL ODOMETRY
Wheel Encoders
Custom encoders on the front two wheels pair Hall effect sensors with neodymium magnets to deliver reliable odometric pulses even when vision struggles — dust, low texture, or motion blur.
● Sensing: Hall effect + neodymium magnets
● Mounting: front two wheels only
● Role: backup odometry when VIO degrades
Odometry is the safety net — not the primary estimate.
INERTIAL SENSING
MPU-6050 IMU
A 6-axis MEMS IMU is mounted flat at the exact geometric center of the chassis deck and sampled at 200 Hz by the Arduino Nano. High-frequency inertial cues feed the back-end to resolve the scale ambiguity inherent to monocular VIO.
● Axes: 6 (3 accel + 3 gyro)
● Sample rate: 200 Hz over I2C
● Mount: chassis-center, flat orientation
Inertial cues are what make monocular SLAM metric, not just geometric.
PS-21 · ODOMETRY & IMU
07
Notes: - Hall effect + neodymium magnets give reliable pulses even in dust, low texture, or motion blur. - Only the front two wheels carry encoders — enough for skid-steer differential odometry at low cost. - IMU sits flat at the chassis geometric center so inertial readings reflect true body motion, not deck flex. - Role split: encoders are the safety net when VIO degrades; IMU is what makes monocular VIO metric.

## Slide 9
02 / 02
Algorithmic Pipeline
Front-end perception, bounded-memory back-end optimization, and terrain reconstruction under the 150 MB ceiling.
Notes: Pivot from hardware to the ROS 2 software pipeline — front-end first, then the bounded-memory back-end, then terrain reconstruction.

## Slide 10
PS-21 · ALGORITHMIC PIPELINE
09 / 12
FRONT-END · VISION PREPROCESSING
From raw frame to trackable keypoints — cheaply.
The front-end runs entirely on the host (ROS 2). It converts each monocular frame to a robust, sparse set of tracked features while staying inside the CPU and RAM budget that the back-end depends on.
01
Grayscale + CLAHE
Frames are converted to grayscale and enhanced with Contrast Limited Adaptive Histogram Equalization. CLAHE tames the extreme lighting, deep shadows, and crater-rim contrast that would otherwise destroy feature stability across frames.
OUTPUT: ENHANCED GRAYSCALE FRAME
→
02
FAST Keypoint Detection
Lightweight FAST corner detector pulls sparse keypoints from the enhanced frame. FAST is chosen for its low CPU cost — leaving headroom for the optical-flow tracker and the back-end optimizer that share the same Pi 4-class host.
OUTPUT: SPARSE KEYPOINT SET
→
03
Pyramidal KLT Tracking
Keypoints are tracked across frames using pyramidal Lucas-Kanade optical flow. The pyramid lets tracks survive larger inter-frame displacements on rough terrain without forcing a full redetection on every frame.
OUTPUT: FEATURE TRACKS FOR VIO
PS-21 · FRONT-END
09
Notes: - CLAHE before detection neutralizes crater-rim contrast and deep shadows that would wreck feature stability. - FAST chosen over ORB/SIFT for its low CPU cost — frees headroom for tracker + back-end on Pi 4. - Pyramidal KLT survives larger inter-frame displacements on rough terrain without full redetection. - Front-end stays under the RAM ceiling by remaining sparse: only a bounded keypoint set lives in memory. - Entire front-end runs on the host under ROS 2 — no offboard processing, no GPU acceleration.

## Slide 11
PS-21 · ALGORITHMIC PIPELINE
10 / 12
BACK-END · BOUNDED-MEMORY OPTIMIZATION
A sliding-window factor graph that refuses to grow.
Sliding-Window Factor Graph
Historical pose optimization is capped by a sliding-window factor graph. Only a bounded set of recent keyframes and their constraints are kept live in the optimization; older keyframes are marginalized out. This guarantees the back-end's working set — and therefore its RAM footprint — cannot grow without bound over a long traversal.
Result: pose optimization stays strictly under the 150 MB RAM ceiling, regardless of mission length.
Chow-Liu Tree Sparsification
Naive keyframe marginalization causes dense matrix fill-in: dropping one keyframe can blow up the constraint matrix and silently exceed the RAM budget. Chow-Liu tree factor sparsification approximates the marginalization with a sparse tree-structured replacement, preserving the most informative pairwise dependencies and discarding the rest.
Result: marginalization stays sparse — no fill-in, no silent RAM blow-up.
150 MB
RAM CEILING (HARD)
SLIDING
WINDOW POLICY
CHOW-LIU
SPARSIFICATION METHOD
PS-21 · BACK-END
10
Notes: - Sliding window is non-negotiable: without it, the factor graph grows unbounded and 150 MB evaporates within minutes. - Fill-in is the silent killer — dropping a keyframe naively makes the constraint matrix dense and blows the budget. - Chow-Liu tree sparsification approximates the marginalization with a sparse tree, preserving the most informative pairwise dependencies. - Takeaway: bounded memory is a property of the algorithm design, not a runtime hope or a tuning knob.

## Slide 12
PS-21 · ALGORITHMIC PIPELINE
11 / 12
TERRAIN RECONSTRUCTION & HAZARD GRID
Sparse features become a top-down map of where not to drive.
STEP 01
2D Delaunay Triangulation
Sparse feature points are synthesized into a 2D Delaunay triangulation. The triangulation is the geometric scaffold that turns isolated point detections into a continuous, locally-connected terrain mesh.
STEP 02
ZNCC Photometric Filtering
Triangle faces are filtered using Zero-mean Normalized Cross-Correlation photometric consistency. ZNCC rejects shadow edges, dust artifacts, and lighting-induced false features before they pollute the hazard grid.
STEP 03
Top-Down Hazard Grid
Surviving triangles are projected into a top-down 2D hazard grid. Each cell tracks three quantities: step height (h), slope (α), and roughness (r) — the three signals a planner needs to decide where the rover can safely go next.
Reference: aerial view of cratered planetary terrain — analogous to the top-down hazard grid PS-21 produces.
Α · SLOPE
R · ROUGHNESS
PS-21 · TERRAIN
11
H.STEPHEIGHT
Notes: - Delaunay before gridding because raw point clouds lack the local connectivity a hazard map needs. - ZNCC protects against shadow edges, dust artifacts, and lighting-induced false features that would otherwise pollute the grid. - Three hazard signals per cell — step height (h), slope (α), roughness (r) — cover the planning-relevant failure modes. - The grid feeds downstream path planning, giving the planner a continuous "where not to drive" mask.

## Slide 13
PS-21 · LOW-COST AUTONOMOUS ROVER
12 / 12
SUMMARY
A bounded-memory autonomy stack, built from cheap parts.
WHAT PS-21 PROVES
✓
VIO at the Edge
Monocular VIO with inertial scale resolution can run on Pi 4-class hardware inside 150 MB of RAM — no GPU, no offboard compute, no tether.
▦
Hazard Mapping in Real Time
Sparse features → Delaunay → ZNCC filter → 2D hazard grid produces a continuously updated top-down map of step height, slope, and roughness.
◫
Built from Commodity Parts
ESP32-CAM, Arduino Nano, MPU-6050, L293D, Johnson motors — every component is cheap and swappable, by design.
NEXT STEPS
01
Field-test VIO drift on extended outdoor traversals.
02
Benchmark RAM footprint under sustained 30+ minute runs.
03
Integrate hazard grid with a downstream path planner.
04
Harden ESP32-CAM Wi-Fi link against dropouts.
PS-21 · SUMMARY & NEXT STEPS
12
Notes: - Restate the three things PS-21 proves: VIO at the edge, hazard mapping in real time, commodity-parts construction. - Walk the four next steps in order — drift testing, RAM benchmarking, planner integration, Wi-Fi hardening. - Close by inviting questions on hardware, algorithm, or integration — flag that these are the three areas most likely to need follow-up. - Emphasize that next steps are deliberately scoped to validate the proof-of-concept, not extend the scope.